3/20/17
CS 310

POLL	LDI R0, KBSRPtr
BRzp POLL
LDI R0, KBDRPtr

...

KBSRPtr .FILL xFE00
KDBRPtr .FILL xFE02

basic input routine

basic output routine
POLL	LDI R1, DSRPtr
BRzp POLL
STI R0, DDRPtr

...

DSRPtr .FILL XFE04
DDRPtr .FILL XFE06

SAVING registers if you are using the above and a register is going to get overwritten.

privilege mode verses user mode
privilege gives more instructions
mode switch from privilege mode to user mode
lc-3 emulates this with the trap mechnicasm

interrupt vectors gets you a pointer to get the address.
up to 256 routines (8-bit trap)
x0000 to x00FF (256)

page 543 has a list of the routines (6 of them)
getc
out
puts
end
putst
halt (trap25)

Trap instructions
trap 1111 0000 trapvect8

where to go
lookup starting address from table; store in PC

to get back
save address of next instruction (current PC) in R7

there are zero extended (zext) becuse you only care about the lower 8 bits.

RET (JMP R7) opcode is the same.

appendix 8 (529)

jump always uses R7 (all ones) (111)

page 223 is trap mechanism operation

before you go to trap you have to store the r7 and when you return you have to restore the r7

page 227:
.ORIG x3000
LD	R2, TERM	; Load negative ASCII ‘7’	LD	R3, ASCII	; Load ASCII difference
AGAIN	TRAP	x23	; input character
ADD	R1, R2, R0 ; Test for terminate
BRz	EXIT	; Exit if done
ADD	R0, R0, R3 ; Change to lowercase
TRAP	x21	; Output to monitor...
BRnzp AGAIN	; ... again and again...
TERM	.FILL	xFFC9	; -‘7’
ASCII	.FILL	x0020	; lowercase bit
EXIT	TRAP	x25	; halt
.END

page 221
x0430 trap vecters are there and x0430 out
x21 out

r1 and r0 are used for input output
page 543 some are used for memory map register

if you write your own subroutines you still have to save and restore any registers you use.

don't use r7 without saving because it has the PC in it.
privilege (system) space verses user (non-system) space

JSR jump subroutine
JSR 0100 1 pcoffset11

(NOP means no op or no operation code)

page 530 is JSR
you can use labels if you don't want to use offsets

JSRR 0100 ....
RET (JMP R7) just like a trap routine

page 231
if you use an offset you can jump 1024 addresses.